## Slide 1
From Inputs to Fatigue-Life Outputs
Everything a solder-joint thermal-cycling study needs, and everything it produces
INPUTS
SIMULATION
OUTPUTS
ANSYS Mechanical APDL · PyAnsys
Component archive (.cdb) — partner ANSYS export
Board layout (Gerber / ODB++) → meshed board
Material properties + solder creep law (SAC305)
Thermal cycling profile (YAML)
Import & merge component + board; remap material IDs
Apply thermal profile; solve nonlinear creep
→ solved result file: pyansys_assembly.rst
Applied temperature profile
Solder creep-strain history (max / mean)
Critical-volume CRACC_zone(t) + 3-D views
Per-cycle strain increment
FATIGUE-LIFE LAW
Nf = C·(Δεcr)⁻ⁿ
All results are written to <sample_dir>/results/